## Slide 1: Flexible I/O in a Rigid World
“FMC” is a trademark of VITA

## Slide 2: FPGA Mezzanine Card (FMC)
VITA Standard (VITA 57) for I/O mezzanine modules optimized to work with a FPGA-based carrier board
  Deliver a stable, straightforward and compatible standard for board developers
Eliminates need for complex protocol logic on mezzanine
  Maximizes data throughput
  Minimizes latency
  Reduces FPGA design complexity
  Minimizes system overheads
Designed to work with industry-standard form-factors
  PCI, PCI-X, VME, cPCI, ATCA, AMC …
www.vita.com/fmc
Notes: 2

## Slide 3: The Problem
FPGA
I/O circuitry B
Connector
FPGA Board with I/O type B
FPGAs are very powerful and flexible
  Large number of I/O pins
  Very high performance, especially for operations that can be parallelized and for repetitive tasks
  Many “hard” and “soft” IP cores available
Because of power and flexibility, FPGAs are often utilized in I/O portions of embedded systems
If I/O changes, the FPGA can be reprogrammed to handle new I/O, but a board respin is required to accommodate new I/O circuitry
No industry standard way to deal with FPGA I/O up to now
FPGA
FPGA Board with I/O type A
Connectors
I/O
circuitry A

## Slide 4: The Solution
Take I/O off of the FPGA baseboard
Put it on a mezzanine card
FPGA
FPGA Board with I/O type A
FPGA
Connectors
I/O
circuitry A
I/O
circuitry B
Connector
FPGA Board with I/O type B

## Slide 5: The Solution
Design FPGA board with mezzanine site
When I/O changes, only mezzanine card changes
FPGA
FPGA Board with I/O type A
Connectors
I/O
circuitry A
I/O
circuitry B
Connector
FPGA
FPGA Board with I/O type B
FPGA
FPGA Board with mezzanine site

## Slide 6: New I/O module standard: FMC – FPGA Mezzanine Card (VITA 57)
I/O mezzanine module optimized to work with a FPGA-based carrier board
Eliminates need for complex protocol logic on mezzanine
  Maximizes data through-put
  Minimizes latency
  Reduces FPGA design complexity
  Minimizes system overheads
    Lower cost
    Lower power
Better thermal characteristics than having the FPGA on a PMC/XMC mezzanine
FPGA
Carrier with FPGA

## Slide 7: FMC – FPGA Mezzanine Card (VITA-57)
Single width module: 69x76.5mm (appr. ½ of PMC)
  Double width variant also defined
Commercial and conduction cooled variants
Low pin count and high pin count connector
  HPC: High Pin Count SeaRay Connector with 400 pins
  LPC: Low Pin Count SeaRay Connector with 160 pins
Flexible interconnect between FMC and FPGA
  Parallel I/O – single-ended or differential pairs
  Up to 10 Multi-Gigabit Transceiver (MGT) high-speed serial links
LPC
.
.
.
160 single ended or 80 differential pairs
.
.
.
10 MGT pairs
JTAG
I2C
Clocks
.
.
.
68 single ended or 34 differential pairs
1 MGT pair
JTAG
I2C
Clocks
HPC
Power
Power

## Slide 8: Comparison, XMC vs. FMC
XMC: 75x150 mm
FMC: 69x76.5 mm

## Slide 9: FMC on a 6U card
One…

## Slide 10: FMC Carrier Example with one FMC site

## Slide 11: FMC on a 6U card
Two…

## Slide 12: FMC Carrier Example with two FMC sites

## Slide 13: FMC on a 6U card
Three!

## Slide 14: Functions suitable for FMC
Analog I/O: ADCs & DACs
Digital parallel I/O: e.g., Camera Link, LVDS, FPDP
Digital High-Speed Serial I/O: e.g., Fiber Optics, SerialFPDP, Gb/10Gb Ethernet
ADC
ADC
ANALOG I/O
ADC
ADC
ADC
ADC
PARALLEL I/O
HIGH SPEED
SERIAL
I/O

## Slide 15: So now there are two I/O module formats
PMC / XMC
  For high-speed Analog and Digital I/O and Fiber-Optics
  Protocol engine (PCI-X, PCI Express, sRIO etc.)
  For use with SBCs
  Established standard – large ecosystem
FMC (VITA-57)
  FPGA Mezzanine Card
  Only I/O front end on module (FPGA sits on carrier)
  HDL code provided to integrate into FPGA design
  Emerging standard

## Slide 16: Sample Products

## Slide 17: FMC Suppliers
 | FMC Modules |  |  |  |  |  |  | Carriers |  |  |  |  |  |  |  | Support |  | 
Company | High Speed Serial | Networking | Image Processing | A/D Converter | D/A Converter | Digital Receiver | RF Transceiver | AMC | VPX | VNX | VME | VXS | PCIe | CompactPCI | Motherboard | Connectors | Bezels | Dev. Platform
4DSP LLC |  |  |  |  |  |  |  |  | 3U |  |  |  |  | 3U |  |  |  | 
Avnet * |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Alpha Data Parallel Systems Ltd |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Annapolis Micro Systems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
BittWare, Inc. |  |  |  |  |  |  |  |  | 3U |  |  |  |  |  |  |  |  | 
Cook Tech * |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CES-Creative Electronic Systems |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Curtiss-Wright |  |  |  |  |  |  |  |  | 3/6U |  |  |  |  |  |  |  |  | 
Faster Technology |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HiTech Global * |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Intel Corporation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Interface Concept |  |  |  |  |  |  |  |  | 3/6U |  |  |  |  |  |  |  |  | 
Kontron * |  |  |  |  |  |  |  |  | 3U |  | 6U |  |  |  |  |  |  | 
Lyrtech |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mercury Systems, Inc. |  |  |  |  |  |  |  |  |  |  |  | 6U |  |  |  |  |  | 
MoSys |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nolam Embedded Systems * |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Nutaq |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Pentek, Inc. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Parsec |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Samtec, Inc. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TechwaY |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Tokyo Electron Device Ltd. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
VadaTech Inc. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Xilinx |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
XTECH |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
* Not FMC Marketing Alliance member

## Slide 18: For more information
VITA FMC Page
  www.vita.com/fmc