The Gb failure rate for ceramic chip CDR capacitors in MIL-HDBK-217 F Notice 2 is 0.0035, I would like to show that a pi-Q factor of 0.1 is reasonable.

Dedicated test cards are used to test production cards.  The test cards (ETS) are KTBG production units and remain in the set up until failure.  When they fail they are repaired and put back into service.  There were 161 dedicated test cards; the total of logged hours on these cards was 157,559,270.  Calculations are detailed below.

This total is insufficient and extra hours are required, so it is necessary to incorporate some field data.

Focusing on PPCs out of a range of products, Radstone shipped over 3500 PPCs in 2005, looking at a particular PPC for a particular customer gives a field population of 1198 boards, out of which 85 were returned in 2005, this figure includes NFFs, but no capacitor failures.

These boards have 349 ceramic capacitors, assume each is used for 600 hours a year (50 weeks at 12 hours per week) over 6 years gives a total of 626,524,800 hours.

|  | FIELD POPULATION | NEW | YEARS | BOARD YEARS |  |
| --- | --- | --- | --- | --- | --- |
| 2005 | 1198 | 300 | 1 | 300 |  |  |
| 2004 | 898 | 300 | 2 | 600 |  |  |
| 2003 | 598 | 300 | 3 | 900 |  |  |
| 2002 | 298 | 298 | 4 | 1192 |  |  |
|  |  |  |  | 2992 | 626,524,800 |  |
|  |  |  |  |  | 600 | HOURS |
|  |  |  |  |  | 349 | CAPS |

Hours logged now, 157,559,270+ 626,524,800 = 641,577,600 which equate to 0.0013 fpmh.  This is not low enough, looking at another product with a field population of 2705 over the previous six years

|  | FIELD POPULATION | YEARS | BOARD YEARS |  |
| --- | --- | --- | --- | --- |
| 2005 | 2705 | 1 | 2705 |  |  |
| 2004 | 2325 | 2 | 4650 |  |  |
| 2003 | 1945 | 3 | 5835 |  |  |
| 2002 | 1565 | 4 | 6260 |  |  |
| 2001 | 1185 | 5 | 5925 |  |  |
| 2000 | 805 | 6 | 4830 |  |  |
|  |  |  | 19450 | 2,567,400,000 |  |
|  |  |  |  | 600 | HOURS |
|  |  |  |  | 220 | CAPS |

Hours logged now, 157,559,270 + 626,524,800 + 2,567,400,000 = 3,351,484,070 which equate to 0.0002984 fpmh.  This is below the product of 0.0035 (for a ceramic chip capacitor) and a piQ of 0.1.

Calculations for the test gear hours below:

|  |  | days | nights | total | pro-rata | per week | 1st three quarters | last quarter | for year | no. years | no. ETS cards | no. racks | capacitors per board | HOURS TOTAL |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 8--5 | 11-8 |  |  |  |  |  |  |  |  |  |  |  |
|  | PPCX | 9 | 9 | 18 | 14.4 | 57.6 | 921.6 | 921.6 | 1843.2 | 6 | 2 | 2 | 273 | 12,076,646 |
|  | ENVIRONMENTAL | 7 | 7 | 14 | 11.2 | 56 | 896 | 896 | 1792 | 6 | 2 | 16 | 360 | 123,863,040 |
|  | NOMINAL PPC | 7 | 7 | 14 | 11.2 | 56 | 896 | 896 | 1792 | 4.5 | 1 | 2 | 349 | 5,628,672 |
|  | NOMINAL PPC | 7 | 7 | 14 | 11.2 | 56 | 896 | 896 | 1792 | 1.5 | 1 | 1 | 349 | 938,112 |
|  | NOMINAL DSP | 7 | 7 | 14 | 11.2 | 56 | 896 | 896 | 1792 | 6 | 1 | 2 | 700 | 15,052,800 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | 157,559,270 |